Tools & supplies

1 1/16 6-point socket

Adapter, ¾” male hose to valve stem “Blow Out Plug”

Air compressor with regulator set to 40psi max

4 gallons anti-freeze (usually takes about 2.5 gal)

Winterizing Montana using anti-freeze

- Drain holding tanks, leave valves open

- Drain water tank

- Drain portable water filter, let filters dry

- Turn “Water Heater Bypass” to the “on” position (horizontal)

- Remove water heater drain/anode 1 1/16” socket, leave out

- Connect the air line to the “Black Tank Flush Valve”, blow out black tank flush, 40psi max

- Connect air line to “City Water Connection”; set regulator to 40psi max

  - Turn the “Fresh Water Tank Power Fill Valve” to the “Fill” position (vertical)

    - Blow water out of the line going to the fresh water tank

    - Turn the “Fresh Water Tank Power Fill Valve” to the “Normal Flow” position (horizontal)

- Connect a short hose to the “Freeze Guard” connection, other end into a container of RV antifreeze

- Turn the winterizing valve to the “on” position (horizontal)

- Turn on water pump, monitor antifreeze container to keep hose submerged. Open each faucet cold then hot, in turn until antifreeze flows

  - Kitchen sink, cold, hot

  - Bath sink, cold, hot

  - Shower, cold, hot

  - Washer, cold, hot

  - Toilet

  - Toilet sprayer

  - Low points

- Make sure antifreeze fills each sink trap

- Shut pump off

- Close faucets

- Open low point drains, verify antifreeze is present

- Close low point drains

- Close water tank drain

- Wipe anti-freeze out of sinks

- Sta-Bil generators, chain saw, etc.

- Put anti-mouse dryer sheets in trailer

- Remove tire pressure monitors

De-Winterizing Montana

- Use clean-out spout to flush out water heater tank

- Connect a short hose to the “Freeze Guard” connection, other end into a container of clean fresh water

- Winterizing valve should still be in the “on” position (horizontal)

- Turn on water pump and pump several gallons through any faucet to clean out water pump

- Turn winterizing valve to the “off” position (vertical)

- Hook garden hose to city water with regulator, turn on

- Open low point drains, run until clear, close low point drains

- Begin running water through all faucets, cold & hot, until clear, run for 1 hour or more

- Install water heater drain/anode, use Teflon tape

- Turn “Water Heater Bypass” to the “off” position (vertical)

- Fill water heater, run some water through it

- Install new water filter

- Sanitize fresh water tank

- Fill fresh water tank

- Check tire pressures

- Install tire pressure monitors

- Change generator oil

- Prep Generators

- CO detector and smoke detector batteries

- Outside thermometer battery

- Grease suspension

Winterizing Montana using air

- Drain holding tanks, leave valves open

- Drain water tank

- Drain portable water filter, let filters dry

- Turn “Water Heater Bypass” to the “on” position (horizontal)

- Remove water heater drain/anode 1 1/16” socket, leave out

- Connect the air line to the “Black Tank Flush Valve”, blow out black tank flush

- Connect air line to “City Water Connection”; set regulator to 40psi max

  - Outside faucet, cold, hot

  - Kitchen sink, cold, hot

  - Bath sink, cold, hot

  - Shower, cold, hot

  - Washer, cold, hot

  - Toilet

  - Toilet sprayer

  - Turn the “Fresh Water Tank Power Fill Valve” to the “Fill” position (vertical)

    - Blow water out of the line going to the fresh water tank

    - Turn the “Fresh Water Tank Power Fill Valve” to the “Normal Flow” position (horizontal)

- Open faucets

- Open low point drains, allow to drain

- Close faucets

- Close low point drains

- Close holding tank valves

- Close water tank drain

- Sta-Bil generators, chain saw, etc.

- Put anti-mouse dryer sheets in trailer

- Remove tire pressure monitors